## Slide 1: Computational Haptics Laboratory
Haptic Memory
Marc Dreiser and Julian Eiler
07.08.2015
Prof. Dr.-Ing. Eckehard Steinbach

## Slide 2: Concept - Quizgame
Game Consists of 4 Phases:
  Initialization: Get an overview over the models (can be skipped)
  Exploration: Touch the object and try to guess the object
  Solving: Three options are displayed and the user should choose one
  Solution: The user is informed, if his choice was correct
Choose number of rounds to play
Display the performance

## Slide 3: Solution Phase

## Slide 4: Concept - Quizgame
Game Consists of 4 Phases:
  Initialization: Get an overview over the models (can be skipped)
  Exploration: Touch the object and try to guess the object
  Solving: Three options are displayed and the user should choose one
  Solution: The user is informed, if his choice was correct
Choose number of rounds to play
Show the user his performance

## Slide 5: 3D Object: Cork

## Slide 6: Voice Coil Actuator
Voice Coil Actuator
Translation

## Slide 7: Voice Coil Actuator
Dynamics of intervening linkages, joints, and cables distort the output of the motors  interferes especially with the display of high freqency vibrations *
Generates vibrotactile frequencies (20-1000 Hz) in real time
Play acceleration file with the Bass library
https://books.google.de/books?id=MMeaI1TMvyMC&pg=PA256&lpg=PA256&dq=phantom+omni+voice+coil&source=bl&ots=xb_XcUQzxx&sig=kQPPNpT3BscUGyFQ3oj-Q3hHIPo&hl=de&sa=X&ved=0CCUQ6AEwAGoVChMIn7qNgeCNxwIVxAiSCh1a-AJU#v=onepage&q=phantom%20omni%20voice%20coil&f=false
* Robotics Research, The 14th International Symposium ISRR

## Slide 8: Force and Velocity measurements
Velocity (V)
Force
(F)
F = const.
V = const.
F = const.
V = const.
Should Haptic Texture Vibrations Respond to User Force and Speed?
Heather Culbertson and Katherine J. Kuchenbecker

## Slide 9: Acceleration file
F = const.
Acceleration [m/s]
Time [s]

## Slide 10: Force and Velocity: Approach 1
Velocity
Force
Five discrete values
Constant
Five soundfiles for different velocities
Amplitude constant (independet of penetration depth /force)

## Slide 11: Force and Velocity: Approach 2
Velocity
Force
Amplitude
Five soundfiles for different velocities
Amplitude linear to penetration depth

## Slide 12: Optimal Design Process
Real Object
Record object properties
Virtual Object
Model object properties
Automatic Filter Design for Synthesis of Haptic
Textures from Recorded Acceleration Data. Kuchenbecker et al.
A Haptic Texture Database for Tool-mediated Texture Recognition and Classification, Strese et al.

## Slide 13: Optimal Design Process
Real Object
Generate Force-Velocity Map for every Position
Virtual Object
Render Object and display force and velocity according to object friction, stiffness and other properties of the real object
Time dependent
?
Values from various literature sources

## Slide 14: Problems
Voice coil actuator
  Not always available
  Not properly working (spring missing)
Acceleration files
  Unknown force and velocity
  Not location based
  Irregular velocity / force
Computational Constraints
  Problems with the haptics loop (play sound files)
  Simple 3D Objects (< 5,000 vertices)

## Slide 15: Result
Simple game logic
12 blender objects with soundfile, stiffness, and friction
2 modes for handling the penetration depth
Created a framework for displaying acceleration files over the sound port of the computer with a voice coil actuator

## Slide 16: Incresing Velocity
Small Velocity
Large Velocity

## Slide 17: 3D Objects

## Slide 18: Voice Coil Actuator
Air gap
Electric coil
Soft Iron
(fixed)
Coil holder
(sliding)
Permanent Magnet

## Slide 19: 3D Objects
Design objects according to the soundfiles we got
Similar in shape in order to make it not too easy
Different in texture

## Slide 20: Our Work
Implement game logic
Create 3D objects
Handle user unputs
Connect voice coil actuator with CHAI 3D